## Slide 2: The RDTZ
Optimising the Southampton Network Architecture
18th April 2018
Simon Lane
Senior Network Architect
iSolutions

## Slide 3: The RDTZ Brief
Perform µViz tests at 1 Gbps
Deploy perfSONAR node alongside µViz datastore
Deploy perfSONAR node outside campus border firewalls
Upgrade µViz datastore to 10 Gbps
Deploy External DTN outside campus border firewalls
Do some tests
Observe impact on the network

## Slide 4: Network Architecture - LAN
Core Switches
4* Cisco Nexus
140* 10 Gbps
Edge Stacks
1,160* Cisco Catalyst
10 / 1 Gbps
Wireless APs
2,800* Cisco APs
a/b/g/n/ac 1.3 Gbps

## Slide 5: Network Architecture - Infrastructure
Ducts
Resilient routes
Avoid major buildings
Fibre
30Km new cables
750Km singlemode fibre
Wide-Area Circuits
BT, Virgin Media, SSE
Up to 10 Gbps

## Slide 6: Network Architecture - External
Border Firewalls
2* Palo Alto 7050
HA failover pair
Internet
2* 10Gbps to JANET
Data Centre
1* 10Gbps to JANET
4* 10Gbps to Highfield

## Slide 7: Local Area Network

## Slide 8: Wide Area Network

## Slide 9: µ-VIS
Principally located in building 5 on Highfield campus
  X-Ray scanners
  Data-store and workstations mostly co-located
  10 Gbps network internally and over fibre to building 54
External facilities
  Diamond Light Source generates large data sets
  up to 20 TBytes for analysis and visualisation locally
Standard 1Gbps University Network connection (CAT 5e)
  may be perceived as too slow or impractical for big transfers
  however the network appears to have some capacity available …

## Slide 10: Capacities – Edge Buildings
Switch stack up to 8 switches (64 Gbps stacking capacity)
48* 1 Gbps ports per switch
2* 10 Gbps to Highfield core (LACP sharing)
Typical switch stack uplink utilisation

## Slide 11: Capacities – Highfield Core
140* 10Gbps interfaces active on each chassis
550 Gbps per slot on chassis
15 Tbps switching capacity
Typical interface utilisation

## Slide 12: Capacities – JANET links
2 Highfield links in use (DC link is disaster recovery)

## Slide 13: Capacities - Firewall
Application Aware Next Generation firewall
Threat signatures updated daily from Global Cloud
Active/Passive stateful failover
About 15 Gbps throughput capability with current blades
10 Gbps external interface, 2* 10 Gbps internal interfaces
Typical firewall throughput

## Slide 14: µ-VIS 1 Gbps Results
Installed Globus on µ-VIS server and tested transfers from Diamond Light Source
Peaked at 900 Mbps

## Slide 15: µ-VIS 1 Gbps Results
However a significant number of packet discards at the 1Gbps port.
Presumed due to buffer overflow in edge stack on transition from 10 Gbps to 1 Gbps

## Slide 16: Packet loss rate at edge switch port
A crude measure, but:
  b5as-stack1#show interface gi4/0/39
  … Total output drops: 556074
  … 4985497775 packets output
  b5as-stack1#show interface gi4/0/39
  … Total output drops: 676678
  … 5050969468 packets output
Could possibly increase the packet buffers to get a few more Mbps but want more than 1Gbps

## Slide 17: perfSONAR
Looks at end-to-end network performance
  packet loss, latency, throughput
Mesh of perfSONAR nodes
Compare inside/outside of UoS network
Is the Research DMZ model likely to be of benefit here?

## Slide 18: Deploy perfSONAR
External server:
  Dell PowerEdge R610 Intel(R) Xeon(R) CPU E5520 @ 2.27GHz (2 CPU, 8 cores) 24GB RAM CentOS Linux release 7.3.1611 (Core)
Internal server:
  Dell PowerEdge R210 Intel(R) Xeon(R) CPU X3470 @ 2.93GHz (1 CPU, 8 cores) 8GB RAM CentOS Linux release 7.3.1611 (Core)
Both built from the perfSONAR Toolkit ISO
Application specific rules in campus firewall where possible (iperf, traceroute, icmp, ssl, web-browsing)

## Slide 19: perfSONAR Results
Diamond to Internal perfSONAR (building 5)
  http://perfsonar.diamond.ac.uk/

## Slide 20: perfSONAR Results
Diamond to External perfSONAR
  http://perfsonar.diamond.ac.uk/

## Slide 21: perfSONAR Results
ps-londhx1.ja.net to Internal perfSONAR (Building 5)
  http://ps-londhx1.ja.net/

## Slide 22: perfSONAR Results
ps-londhx1.ja.net to External perfSONAR
  http://ps-londhx1.ja.net/

## Slide 23: perfSONAR Results
From diamond to internal and external perfSONAR
  throughput quite erratic 1  5 Gbps
  packet loss typically <0.02%
From JANET to external perfSONAR
  throughput fairly consistent 6  7 Gbps
  zero packet loss most of time, good for high RTT transfers
From JANET to internal perfSONAR
  firewall / LAN introduces small loss, typically <0.02%
  throughput more erratic than external node 4  8 Gbps
  higher peak may be result of CPU differences in perfSONAR nodes

## Slide 24: Network Hiccup
Content update affects iperf throughput tests
Palo Alto content update released and withdrawn
Palo Alto software upgrade

## Slide 25: perfSONAR Conclusions
Should be able to get > 1Gbps to internal hosts, but may be quite erratic – day/night, term/vacation
Firewall / LAN introduces some packet loss
Hosts outside the firewall could perform more consistently well due to low packet loss and no contention on firewall interfaces

## Slide 26: µ-VIS 10 Gbps connection
Upgrade µ-VIS to 10 Gbps campus connection
  CAT 5e cable will not do 10 Gbps
  spare single-mode fibre available to µ-VIS
  spare 10 Gbps port on edge switch stack…
  … plug it in
Some operational concerns as had not deployed 10 Gbps to “user space” before.
  short tests initially
  monitoring systems alerted to high utilisation
  no other impact observed

## Slide 27: µ-VIS 10G Globus Results
Richard will say more about the results achieved
Early test below shows 4 concurrent streams up to 4 Gbps

## Slide 28: µ-VIS 10G Globus Results - Firewall
Firewall external interface peaking to 9.2 Gbps
No detrimental effects observed

## Slide 29: Deploy External Globus DTN
Server to hand
  Dell PowerEdge 720 24 CPUs x 2.399 Ghz (2 socket 12 core) Intel XEON CPU E5-2695 256GB Memory 300 GB SSD, 2TB HDD Intel X520 10Gb/SFP+
  Red Hat Enterprise Linux 7
Globus Connect Server https://docs.globus.org/globus-connect-server-installation-guide
iptables on host, packet filtering rules (acl) in external switch

## Slide 30: External Globus DTN
Deployed as test device only
  server hardware probably not optimal for task
  not integrated with UoS user accounts
  only 2 TByte hard disk, 300 MByte SSD
  no direct access to any shared filestore
  no service resilience
In current form, can use as a staging post
  to work around high RTT, lossy paths perhaps

## Slide 31: External DTN results
10 GByte file from CERN to a test host (VM) in the DataCentre staged via the DTN, compared to direct.

## Slide 32: Project Observations
Capacity of external firewall interfaces probably limiting factor right now
  high capacity firewalls and core LAN equipment are expensive
  does the value of inspecting a flow diminish for big flows?
perfSONAR measures network performance, and can identify changes in network behaviour affecting large data transfers
  Understanding packet loss through the firewall and LAN equipment is difficult
A basic Globus DTN was easy to set up, and easy to use
  Globus desktop is equally easy

## Slide 33: Project Observations
No negative impact from perfSONAR or Globus transfers
  TCP played nicely so far
We haven’t done any work at the DataCentre – where our HPC and most of our storage reside
The Science DMZ could be built at Southampton
  we have physical infrastructure across the Highfield campus
  requires resources to design, build and monitor
  requires understanding of security issues
  how do you get the data out of the DMZ once on-site?
  which campuses would need it and how would we reach them?
  do you need it?

## Slide 34
Simon Lane
Senior Network Architect
iSolutions
S.J.Lane@soton.ac.uk